## Slide 1
File Formats of Neuroimaging
John Muschelli
Johns Hopkins Bloomberg School of Public Health
January 26, 2015

## Slide 2: Image formats: DICOM
DICOM (Digital Imaging and Communications in Medicine) format Standardized way of representing images
Usually how data is given either from scanner or hospital PACS (picture archiving and communication system) system 2 integral pieces: Image data (in pixels) and header
(meta-data (data about data))
Think of a JPEG and a text file

## Slide 3: DICOM pixel data
The pixel data in a DICOM file is a matrix (fixed number of rows and columns).
One DICOM file represents one ”slice” of the brain.
The oro.dicom package is good for reading in this data.
library(oro.dicom)
slice = readDICOM('Example_DICOM.dcm') class(slice)
[1] "list"

## Slide 4: readDICOM output
The output is a list with 2 elements: the DICOM header (hdr) and image (img) information, both of which are lists.
Each element of hdr has a data.frame, and the elements of img
are matrices:
names(slice) [1] "hdr" "img"
class(slice$hdr) [1] "list"
class(slice$hdr[[1]]) [1] "data.frame" class(slice$img)
[1] "list" class(slice$img[[1]]) [1] "matrix"

## Slide 5: Display DICOM Image
We can display the data using the image command.
(We transpose the data using t() so the image faces “up” instead of “right”.)
image(t(slice$img[[1]]), col=gray(0:64/64))

## Slide 6: DICOM Header Information
What about the header?
There are many fields, for example pixelSpacing, which is the dimensions (x and y) of a pixel in millimeters (mm):
hdr = slice$hdr[[1]]
hdr[ hdr$name == 'PixelSpacing', "value"]
[1] "0.46875 0.46875"

## Slide 7: Multiple DICOM files
We have discussed only one slice of the brain. What about multiple slices? If you pass a directory into readDICOM, it will read in all DICOM files in that directory.
all_slices = readDICOM('T1/')

## Slide 8: NIfTI
Now that we have multiple slices read in, we can convert it to a 3-dimensional (3D) array, where you can think of the array as stacking each slice (which is a matrix) on top of each other. If each DICOM is a piece of paper, the 3D array is a stack of paper. The way we store this 3D array is in the NIfTI (Neuroimaging Informatics Technology Initiative) format.
DICOM NIfTI
File extension: Each file is a: Header informa- tion: Different Images
.dcm
.nii or .nii.gz (compressed)
slice of the brain
Many fields, protected health information, hospital- related meta-data
Different Folders
3D image of brain
Image meta-data, no patient information
Different Files (can be same directory)

## Slide 9: NIfTI
We can convert this list of header information and image information to a nifti object (an R object) with the dicom2nifti command:
nii = dicom2nifti(all_slices) dim(nii); class(nii)
[1] 512 512 22
[1] "nifti"
attr(,"package")
[1] "oro.nifti"
We can see that this nii object is indeed a nifti object and has 3 dimensions.

## Slide 10: Writing out NIfTI file
The writeNIfTI command from the oro.nifti package can write out this nifti object to a NIfTI file:
library(oro.nifti)
writeNIfTI(nim = nii, filename = "Output_3D_File") list.files(getwd(), pattern = "Output_3D_File")
[1] "Output_3D_File.nii.gz"
Note that the extension is .nii.gz, which is a compressed NIfTI file, which saves disk space for storage.
You can output a non-compressed file using the argument
gzipped=TRUE.
(NB: The filename argument in writeNIfTI should NOT have an extension)

## Slide 11: Other DICOM converters
Although our main goal is to analyze neuro data with the fewest pieces of software, we are pragmatic and use existing software if it works well.
The dcm2nii software converts DICOM files to NIfTI files, and can handle many different formats and file types.
In general, the format we will be using will be NIfTI, and we will store out data in compressed format, so extensions of our images will be .nii.gz.

## Slide 12: Other formats
For Philips scanners, files from the scanner are PAR/REC and not DICOM. r2a can convert these to NIfTI.
NIfTI format was based on ANALYZE format where the header and image were in separate .hdr and .img files. This is an older fromat and we will not use this way of storing data because 1) NIfTI can have one file with both header and image information, and 2) Can be stored as compressed .nii.gz files.
NRRD (Nearly Raw Raster Data) is another format similar to NIfTI. Much of the neuroimaging software can read in both NRRD and NIfTI files, but NIfTI is much more common.